## Slide 2: Watershed Advisory Committee Lake Erie Direct Tributaries Chagrin River March 2019

## Slide 3: Agenda
Sewer District Updates
  Community Cost-Share
  Local Sewer System Evaluation Studies
  Member Community Infrastructure Program
  Acquisitions, Demolition & Property Owner Communications
Stormwater Master Plan
Stormwater Inspection and Maintenance
  State of the Infrastructure
  2018 Maintenance Summary
  2019 Small Scale Projects
Stormwater Construction Plan
  2018 Stormwater Highlights
  Project Prioritization
  Stormwater Design Projects
  Stormwater Construction Projects

## Slide 4
CCS Funds Balance (8/31/2018) $ 22,039,931
67 approved projects $ 9,150,615
17 approved allocation agreements $ 7,539,502
CCS Funds available to Member Comm. $ 5,349,814
30 of 55 Member Communities currently participating
Community Cost-Share
Update
Notes: NEORSD Proposed Stormwater Program October 2009
4
Highlight 3 points on community cost-share
-Need an approved application and executed agreement before a project begins
-Consider an allocation for larger projects to allow for reimbursement over a the next 5 years
-If your CCS project is complete request a reimbursement!

## Slide 5: Community Cost-Share Project Ideas
Update

## Slide 6: Local Sewer System Evaluation Studies
Heights Hilltop Interceptor (HHI) Combined Sewershed
Mill Creek Interceptor (MCI)
Southwest Interceptor (SWI) Cuyahoga Valley Interceptor (CVI)
community work plans
field work
modeling/
alternatives
field work
modeling/
alternatives
Update
Notes: Each WTL to speak to the LSSES in the area. Provide a brief verbal update.

## Slide 7: Sewer System Evaluation Studies
Heights Hilltop Interceptor (HHI)
Combined Sewershed
Mill Creek Interceptor (MCI)
Southwest Interceptor (SWI)
Cuyahoga Valley Interceptor (CVI)
Update
Notes: Each WTL to speak to the LSSES in the area. Provide a brief verbal update.

## Slide 8
South Euclid Community Cost Share – Equipment Purchase
Questions

## Slide 9: Stormwater Master Plan

## Slide 10: Stormwater Master Plan Study Process
Notes: The consultant will identify problem areas by conducting a geomorphic assessment of the open channel system and an asset condition assessment for RSS parent assets, BTU child assets, and any LSS assets that directly influences the condition of the RSS asset. An asset condition rating score will be assigned to each asset for each of the following three asset management categories:
Sediment and debris accumulation – which focuses on the percent of flow area or storage volume filled with sediment or debris through field inspection;
Structural integrity – assessed through field inspections and H/H models. The structural integrity assessments include both the geomorphologic assessment for streams and structural assessment of engineered materials for the other asset class types;
Hydraulic performance – an assessment of the probability that asset class types surcharge or result in flooding of structures and roads.
The combination of the assigned asset condition rating with pre-assigned criticality values generate a business risk evaluation (BRE) score for each RSS to identify problem areas within each subwatershed. The standards for determining the asset condition and developing the BRE scores is presented in detail in section 3 of the SWMP standards (Attachment 2).
The end product of the SWMPs is a prioritized list of construction, operation and maintenance, and policy improvements to improve water quality, enhance stream health and function, and protect resources, and reduce flooding and erosions risks related to RSS assets.
In general, this project should include the following components:
An Operational Performance Evaluation that includes field inventory (where necessary), assessment, monitoring, and modeling to characterize existing conditions and identify problems within the RSS and potentially the local stormwater system, when necessary.
An Alternative Development and Evaluation process that systematically develops a comprehensive set of solutions to existing and projected stormwater problems within the watershed and subwatersheds, including the business case for the recommendations.
Development of a Stormwater Master Plan that identifies recommendations, including phasing recommendations, for prioritized policies, construction projects, acquisition strategies, and maintenance activities necessary to implement preferred alternatives.
Stakeholder Involvement to support the SWMP process, engaging both District staff and the Watershed Advisory Committee (WAC) and its members to assist in facilitating effective feedback for a successful plan.
This slide provides an overview of the process and activities for this study.

## Slide 11
Stormwater Master Planning
(status through 2/25/2019)
Chart: Cuyahoga River South
| Stormwater Master Plan | Alternatives Development | RSS Modeling | Condition Assessments | Field Investigations | Data Collection & Review
Complete | 0.988 | 1 | 1 | 1 | 1 | 1
Remaining | 0.012 | 0 | 0 | 0 | 0 | 0
Chart: Cuyahoga River North
| Stormwater Master Plan | Alternatives Development | RSS Modeling | Condition Assessments | Field Investigations | Data Collection & Review
Complete | 0.0764 | 0.5533 | 0.7784 | 1 | 1 | 1
Remaining | 0.9236 | 0.4467 | 0.2216 | 0 | 0 | 0
Chart: Rocky River
| Stormwater Master Plan | Alternatives Development | RSS Modeling | Condition Assessments | Field Investigations | Data Collection & Review
Complete | 0.1255 | 0.2824 | 0.6804 | 0.8709 | 0.8709 | 0.8709
Remaining | 0.8745 | 0.7176 | 0.3196 | 0.1291 | 0.1291 | 0.1291
Chart: Chagrin/Lake Erie
| Stormwater Master Plan | Alternatives Development | RSS Modeling | Condition Assessments | Field Investigations | Data Collection & Review
Complete | 0 | 0.1 | 0.04 | 0.1076 | 0.1076 | 0.1076
Remaining | 1 | 0.9 | 0.96 | 0.8924 | 0.8924 | 0.8924
Completion Date: April 2020
Completion Date: May 2021
Completion Date: April 2019
Completion Date: November 2019

## Slide 12: Stormwater Master Plan Study Area
Total Study Area
217,318 acres (58,616 within SWSA)
25 Subwatersheds in the SWSA
21 WAC Member Communities
Chart: 
| Completed | 2nd Qtr
Sales | 7 | 93 | 0 | 0
7% Complete

## Slide 13: Stormwater Master Plan Field Work Project Status
Task Item Status – 11% Complete
Survey work (321 cross sections)
Culverted Stream Inspection (33.15 miles)
  23.3 miles within Combined Sewer System Area
Open Channel Streams (59.6 miles)
Inventory Crossings (321 total)
Basins (30 total)
High Water Mark Monitoring
Spherical Imagery
  100 stream miles (CHALET Watersheds)
  15 miles (Cuyahoga & Rocky River Watersheds)

## Slide 14: Stormwater Master Plan Chagrin River / Lake Erie Direct Tributaries
Significant work: thru March 2019
SWMP Project Kickoff
Review of Background Information
Data Collection & Management Plan Dev.
Community Work Plan Development
Culvert Inspections
  Euclid Creek
  Doan Brook
  Dugway Brook - East
Work on Early Action Projects
  Shaker Lakes Nature Center
  Lower Shaker Lake Dam
  Worton Park Drive Neighborhood
CHALET SWMP Project Budget: $10M

## Slide 15: Stormwater Master Plan Upcoming Milestones
Data Collection Activities
  Member Community Work Plans
  HWM Gauge/Level Meter Placement Notifications
SWMP Field Activities
  HWM Gauge/Level Meter installation & Monitoring
  Geomorphological Surveys
  Stream & Basin Surveys
  Spherical Imagery Collection
  Culverted Stream CCTV Inspections Continuation
Model Development
  Watershed Delineation
  RSS Terminus Extension Identification

## Slide 16
Stormwater Master Plan
Early Action Project Area Evaluation
Nature Center at Shaker Lakes
Notes: EAP Background
Nature Center @ Shaker Lakes plans to construct improvements to the existing All People’s Trail boardwalk that has exceeded design life during the 2019 construction season.
NEORSD wanted to determine if the existing boardwalk and the planned improvements would have a impact on the conveyance of Doan Brook. NEORSD also wanted to determine if Doan Brook would have a negative impact on the boardwalk improvements.

## Slide 17
Stormwater Master Plan
Early Action Project Area Evaluation
Nature Center at Shaker Lakes
Notes: The Wade Trim Team (two geomorphic experts and a two-person Collective Efforts inspection crew) conducted a detailed inspection of the Doan Brook reach at the Nature Center at Shaker Lakes (Nature Center) on November 15, 2018. The inspection team walked the boardwalk and nearby trails to observe the overall stream and wetland environment at the Nature Center. Wade Trim submitted a technical memo addressing the findings of the project area evaluation, which included the following:
The condition of Doan Brook where the proposed construction activity will be taking place is fully functional and no building, transportation, or utility (BTU) assets are threatened by erosion. This is primarily because most of the boardwalk is in a low-gradient, wetland environment that is less prone to significant hydraulic erosive forces.
The Nature Center might wish to consider a few relatively minor adjustments to the proposed boardwalk improvements, including extending the boardwalk abutment depth; keying the vortex rock weirs into the banks; and modifying a few aspects of the design to improve habitat conditions.
The condition rating of Doan Brook in the reach immediately upstream of the proposed construction activity is not fully functional and a gravel trailpath BTU is threatened due to vertical instability of the channel. The preliminary business risk exposure score is 20.
The proposed construction activity does not address the threatened gravel trailpath BTU and therefore the District might wish to partner with the Nature Center to take advantage of the upcoming construction work. Two alternatives to address the vertical instability would be to (1) armor the existing stream bank at the point of erosion or (2) re-align the channel so that the erosive flows are directed away from the BTU.

## Slide 18
Stormwater Master Plan
Early Action Project Area Evaluation
Nature Center at Shaker Lakes
Notes: In January, 2019, The District met with Nature Center representatives & their design consultant to discuss the findings of the technical memo and to explore the possibility of partnering with them to address the vertical instability along the stream bank. Due to construction limitations, it was determined that the stream restoration work would not be performed as part of the boardwalk upgrade construction. The District also explored the possibility of performing the work under one of its existing maintenance contracts and revisited the site to determine if this option was viable. After conducting a site visit it was determined that the restoration work was too large for this type of contract. The District also found out during the site visit that there were flooding issues immediately upstream at the S. Park Blvd crossing. Based upon this information, the District determined that the best approach at this time was to finish the overall SWMP study and address this area as a problem area in which alternative evaluations would be further studied and scored to determine the best approach to address the overall flooding & erosion issues in this area.

## Slide 19: Stormwater Master Plan Community Communication
Meet with communities
  Problem Area Review
Recommendations and Community Report
Your Watershed Team Leader serves as the point of contact between the communities and the District

## Slide 20
Questions

## Slide 21: Stormwater Inspection and Maintenance (SWIM)

## Slide 22: SWIM Agenda
State of the Infrastructure
2018 Maintenance Summary
2019 Small Scale Projects

## Slide 23: Westside SWIM Team
Eastside SWIM Team
Keith McClintock Supervisor
Jon Brauer Inspector
Anne Roberto Inspector
Mark Hornyak Project Coordinator
Eric Baker Data Maintenance Administrator
Mark Link Supervisor
Christina Silea Inspector
Nikki Velez Inspector
Claire Posius Project Coordinator
Martina Jozanovic Data Maintenance Administrator

## Slide 24: Questions
Notes: Erosion through residential property where banks are mowed to the edge. Small scale bank stabilization project under SWIM is being pursued to lay banks back to a stable slope and place vegetative cover. About 15” of bank loss in 1 year from 2017-2018. Total length is about 200’.

## Slide 25
Stormwater Design and
Construction Program

## Slide 26
Questions
Notes: Revegetate the slopes and floodplain with native materials that help to hold soils, dissipate energies, trap sediment and provide habitat thereby reducing the threat of the erosion and improving water quality.

## Slide 27: What’s Next
Next WAC Meeting – October 2019

## Slide 28: WTL Contact
Meiring Borcherds
216.881.6600 Ext. 6159 Cell: 440 409 1766
borcherdsm@neorsd.org
Stormwater Program: Community Resources
http://www.neorsd.org/communitystormwaterresources.php